## Slide 1
Departement of Clinical Pathology
Notes: <number>

## Slide 2: COMPLETE BLOOD COUNT
Consists of series of tests:
Hemoglobin
Hematocrit
Mean corpuscular volume (MCV)
Mean corpuscular hemoglobin (MCH)
Mean corpuscular hemoglobin concentration (MCHC)
Red blood cell distribution width (RDW)
White blood cells count
Red blood cells count
Platelets count
Erithrocyte sedimentation rate
Blood smear evaluation
Notes: <number>

## Slide 3: Hemoglobin
The Hemoglobin concentration (Hb) of a solution may be estimated by measurement of its:
Color , ex:
- Hb Sahli
- Cyanmethaemoglobin (internationally
recommended method)
Power of combining with oxygen and carbon monoxide  impractical for routine purposes
Iron content  impractical
Notes: <number>

## Slide 4: Hematocrit/ Packed Cell Volume (PCV)
The hematocrit X 1000 is about 3 times the hemoglobin expressed in g/l
Hematocrit is the volume of erythrocytes expressed as a percentage of the volume of whole blood in a sample
Notes: <number>

## Slide 5
Erythrocyte index
1. MCV =
∑ ery (million)/mm3
Hematocrit
Normal = 80 – 100 fl
=
45 %
5 million/mm3
> Normal = Macrocytic
< Normal = Microcytic
2. MCH =
Hb (g/dl)
∑ ery (million)/mm3)
Normal = 26 – 32 pg
< Normal = Hipochrome
X 10 = . . . . fl
X 10 = . . . . pg
X 10 = 90 fl
Notes: <number>

## Slide 6
3. MCHC =
Hb (g/dl)
Hematocrit (%)
X 100 = . . . g/dl
Normal 32 to 36%
< Normal = Hipochrome
Manual examination  MCHC value more sensitive
Examination by autoanalyzer  MCH value more sensitive
Increased in: HbC dis, hereditary spherocytosis, sickle cell dis
Notes: <number>

## Slide 7
Red Cell Distribution Width (RDW)
Examination of erythrocyte volume heterogenity, reflect the range of erythrocyte shape.
Normal Range = 11.6 to 14.6 %
Correlates with the degree of anisocytosis.
May differentiate thalassemia from iron deficiency.
Notes: <number>

## Slide 8: Erythrocyte sedimentation rate (ESR)
The erythrocyte sedimentation rate (ESR) is the rate at which red blood cells precipitate in a period of 1 hour.
When anticoagulated blood is allowed to stand undisturbed for a period of time, the erythrocytes tend to sink to the bottom.
Two layers are formed, the upper plasma layer and the lower one of red blood cells.
Notes: <number>

## Slide 9: Erythrocyte sedimentation rate…
Test based on: inflammatory and necrotic processes cause an alteration in blood proteins  aggregation of RBCs  heavier and more likely to fall rapidly
Referance values :
Men : 0-15 mm/h
Women : 0-20 mm/h
Child : 0-10 mm/h
Increased by any cause: acute and chronic inflammation, including infections, cancers, and autoimmune diseases
Notes: <number>

## Slide 10: Leukocyte
Leukocytosis (abnormally high count) may be caused by:
a. Systemic or local infections (usually due to bacteria). These counts are highly variable and not diagnostic.
b. Dyscrasia of blood-forming tissues. This is not caused by any known bacteria, but is due to a malfunctioning of the marrow and lymph tissues, resulting in extremely high white cell counts, which sometimes exceed 1,000,000/mm3. Ex: chronic myelocytic leukemia
<number>
Notes: <number>

## Slide 11: Platelets
Platelets are small fragments of cytoplasm derived from megakaryocytes.
On average they are 1.5–3.5 μm in diameter
Normal range varies slightly between laboratories: 150,000 to 400,000/cmm (150 to 400 x 109/liter).
Normal platelets population
Notes: <number>

## Slide 12
Table 1.Manual differential reference range for adults and infants
Notes: <number>

## Slide 13
Eosinophil
Neutrophil
Monocyte
Basophil
Lymphocyte
5 DIFF
Notes: <number>

## Slide 14
Notes: <number>

## Slide 15: Reticulocyte
The reticulocyte count is the most effective means of assessing red cell generation or response to anemia.
Reticulocytes are red cells that are nonnucleated and that contain remnant RNA material, reticulum. Reticulum cannot be visualized by Wright’s stain
Notes: <number>

## Slide 16
Acidophilic Erythroblast
Reticulocytes
Erythrocytes
Enucleation process
RNA +++
RNA ++
RNA +
RNA -
Reticulocyte Count = 0.5 to 2.5 %
Notes: <number>

## Slide 17: Procedures of Leucocyte Differential Counting & Blood Smear Evaluation
Notes: <number>

## Slide 18: Making a blood smear
Place a small drop of well-mixed blood in the centre line of a slide about 1 cm from one end.
Without delay, place a spreader in front of the drop at an angle of about 30o to the slide; move it backwards to make contact with the drop.
The blood should run quickly along the contact line.
Notes: <number>

## Slide 19
With a steady movement of the hand, spread the drop of blood along the slide.
The spreader must not be lifted off the slide until the last trace of blood has been spread out; with a correctly sized drop the film should be about 3 cm in length.
Notes: <number>

## Slide 20
It is important that the film of blood finishes at least 1 cm before the end of the slide.
After the film has been made, let it dry in the air.
Write the patient's identification (and date if appropriate) in pencil on the edge of the film at its origin.
Notes: <number>

## Slide 21
Making a Blood Smear
Notes: <number>
<number>

## Slide 22: Good blood smear
Have counting area.
Leucocyte types can be differentiate
No staining clot
Notes: <number>

## Slide 23: Wright Staining
Staining the blood smear highlights the differences among the different types of leukocytes for easier recognition during the counting process.
The most popular stain: Wright’s stain.
Wright’s stain is a methyl alcohol (methanol) solution of an acid dye and a basic dye. The acid dye in Wright’s stain is known as eosin and is red in color.
Notes: <number>
<number>

## Slide 24: Procedure
Air dry slides on the rack.
Give 12 drop of Wright stain, wait for 2 min
Give 12 drop of buffer solution with pH 6.4, blow and then let stand for 20 min
Wash in running tap-water
Allow to dry.
Notes: <number>
<number>

## Slide 25
Wright Staining
Notes: <number>
<number>

## Slide 26: Leucocyte Differential Counting
Principle: It is count 100 leukocytes on blood film, and the differentiate to the type of leukocyte (in %).
Notes: <number>

## Slide 27
 | EO | BA | ST | SEG | LI | MO | 
1 |  |  |  |  |  |  | 
2 |  |  |  |  |  |  | 
3 |  |  |  |  |  |  | 
4 |  |  |  |  |  |  | 
5 |  |  |  |  |  |  | 
6 |  |  |  |  |  |  | 
7 |  |  |  |  |  |  | 
8 |  |  |  |  |  |  | 
9 |  |  |  |  |  |  | 
10 |  |  |  |  |  |  | 
% |  |  |  |  |  |  | 
Determine the counting area with 10 x objective.
Drop the immerse oil and count with 100 x objective
Procedure
Notes: <number>
<number>

## Slide 28
 | EO | BA | ST | SEG | LI | MO | 
1 | I |  |  | IIII I | II | I | 10
2 |  |  | II | IIII | III | I | 10
3 |  |  |  | IIII IIII |  |  | 10
4 | I |  |  | IIII | IIII | I | 10
5 |  |  |  | IIII III | II |  | 10
6 |  |  |  | IIII IIII |  |  | 10
7 |  |  |  | IIII IIII |  | I | 10
8 |  |  |  | IIII III | II |  | 10
9 |  |  |  | IIII I | IIII |  | 10
10 |  |  |  | IIII II | III |  | 10
% | 2 |  | 2 | 72 | 20 | 4 | 100
Inspect the film from the head to the tail, and then move to the next strip. Examine one or more additional strip until at least 100 cells have been counted
Write down in the first row the first 10 leucocytes counted and do so until the 10th row
Notes: <number>
<number>

## Slide 29
Counting area
10x Objective
Notes: <number>
<number>

## Slide 30
Reporting the differential leucocyte
The differential count expressed as the percentage of each type of cell (Eosinophil, Basophil, Band (Stab) cell, Segmented cell, Lymphocyte, Monocyte), should be related to the total leucocytes count and the result is reported in percent [%]
Notes: <number>
<number>

## Slide 31
Eo / Ba / St / Seg / Ly / Mo / Immature cell(s)
2 - 10 60 20 4 4 %
Blood film Evaluation :
- Erithrocyte : chromation, size, morphology
- Leucocyte : total number estimation
- Thrombocyte : total number estimation (normal: 8 –10/field)
Notes: <number>

## Slide 32
In the counting Area
Obj 10 X:
Leuco: 20 – 30 / f ∞ 5,000 / cmm
40 – 50 / f ∞ 10,000 / cmm
Obj 100 X:
Thrombo: total number in 10 field X 2,000 = no. thrombo/cmm
Notes: <number>
<number>

## Slide 33
Notes: <number>